## Slide 1
Lab Book 0.3. Circuits and Compact Models
Student:

## Slide 2: Instructions General
SOFTWARE
Python notebook supplied by instructors
SCRIPTS
From Github Desktop  Open in Visual Studio Code
Navigate to training/IPSP/Lab3/030_Circuits_&_CompactModels.ipynb
Either run locally or Cloud
Devices to be studied:
Ring Resonators (RR)
Mach-Zehnder Interferometer (MZI)

## Slide 3: Learning outcome #1a – Perfectly balanced MZI
INSTRUCTOR:
Present Python and GDSFactory implementation of the Compact Models and Circuit Model
Describe how to simulate usin SAX library
Describe the outputs.
ALL EXAMPLE #1:
wvl [1500-1600] step 0.001
dL = 0
Kin = Kout = 0.5 for all wvl
Document and comment your results
MZI transfer functions
Paste plot here

## Slide 4: Learning outcome #1b – Unbalanced MZI
HINTS:
wvl [1500-1600] step 0.001
dL = 100 µm
Kin = Kout = 0.5 for all wvl
Comment results: describe the transfer function, which is the FSR? How is it related to the length difference among arms?
Show a numeric calculation of the FSR and length difference matching the results in the graph,
MZI transfer functions
Paste plot here

## Slide 5
Comment results:
MZI transfer functions
Paste plot here
Hints:
wvl [1500-1600] step 0.001
dL = ? µm calculate for FSR = 2 nm
Ka = Kb = 0.5 for all wvl
Your design justification
Write equations / numbers
Learning outcome #2 – MZI Design
Design a MZI with FSR = 10 nm at 1550 nm

## Slide 6
Learning outcome #3 – Delay imbalance with loss
Fringe visibility
Comment results: describe the transfer function, is there any interference pattern in case 1? Is there any interference pattern in case 2? Explain the difference between both cases. Compare the Extinction Ratio of both variations.
Extra: What coupling coefficient will you select for the input coupler if you want to match the losses of the longer arm? Simulate and extract the ER.
Hints:
wvl [1550-1550.5] step 0.0000005
Silicon waveguide model:
n_eff = 2.38,
n_g = 4.25,
D=0,
L_base=1000
dL = L_base + 55960.0840224255;
loss = 4 dB / cm
Case 1. Simulate for Ka = Kb = 0.5 for all wvl
Case 2. Simulate for Ka=0.1 for all wvl
Kb=0.5 for all wvl
MZI transfer functions
Paste plot here

## Slide 7: Thank you